## Slide 1
Longest
Common Subsequence:
Recursive Approach
A recursive path to the optimal subsequence
Generated using CANVA

## Slide 2
What is the Longest Common Subsequence?
The longest subsequence that appears in two sequences in the same order, but not necessarily contiguously.
Example: LCS of “AGGTAB”
and “GXTXAYB” is “GTAB”
Widely used in diff tools, bioinformatics, and version control.
SEQUENCE 1
A
G
G
T
A
B
SEQUENCE 2
G
X
T
X
A
Y
B
LONGEST COMMON SUBSEQUENCE
G
T
A
B

## Slide 3
Recursive Approach to LCS
Solve LCS by breaking the problem into smaller subproblems.
If either sequence is empty, the LCS length is 0.
Characters match
Add 1 and recurse on both sequences without their last characters.
Take the maximum of recurring by dropping the last character from either sequence.
This recursion has exponential time complexity.
int LCS(string X, string Y, int m, int n)
if (m == 0 |l n == 0)
return 0;
if (X[m-1] == Y[n-1])
return 1 + LCS(X, Y, m-1, n-1);
return max(
LCS(X, Y, m-1, n),
);
LCS(X, Y, m, n-1)
Characters differ
Base case
{
}

## Slide 4
Step-by-Step Example
Recursive process for sequences “ABC” and “AC”
Start by comparing the full sequences
ABC vs AC
Branch recursively based on character match
Break down into smaller subproblems
until a base case is reached
Build the solution back from the base cases to get the longest common subsequence
ABC
AC
B ≠ A
C = C
BC
AC
B ≠ A
C = A
AB
A
A = A
C
AC
("AC”)
1
B
A
("A”)
("A”)
(empty)
0
AB
B ≠ A
1
1
B

## Slide 5
Summary &
Key Takeaways
LCS finds the longest common
subsequence between two strings.
Recursive approach is intuitive but
inefficient for large inputs.
Understanding recursion lays the
foundation for dynamic programming.
Explore memoization and DP
techniques next.

## Slide 6
Thank You.